## Slide 1: New Ablation Technologies: In the Future…
Jaemin Shim, MD, PhD
Arrhythmia Center,
Korea University Anam Hospital, Seoul, Korea
Dec 3, 2022
VT Symposium 2022

## Slide 2
Newer Methods for VT Ablation
To improve RF lesion
  Half-normal saline irrigation
  Simultaneous unipolar RF ablation
  Bipolar RF ablation
  Intramural needle ablation
Alternatives to RF
  Retrograde ethanol ablation
  Cryoablation
  Laser ablation
  Shock-wave catheter ablation
  Stereotactic radioablation
  Pulsed field electroporation

## Slide 3
Half-normal Saline Irrigation
Stevenson WG, et al. Can J Cardiol. 2022.
Decreasing the ionic content of the fluid surrounding the catheter-tip electrode increases the resistance of current flow through the surrounding blood, increasing preferential current delivery into the myocardium.

## Slide 4
Half-normal Saline Irrigation
Chung FP, et al. J Cardiovasc Electrophysiol. 2019;30(9):1508-1516.
Out of 160 OT‐VA cases (51±15‐year‐old, 62 males), 31 underwent HNS irrigation after a failed standard NS‐irrigated ablation
Additional acute success in 21 of 31 (67.7%) patients

## Slide 5
Half-normal Saline Irrigation
Chung FP, et al. J Cardiovasc Electrophysiol. 2019;30(9):1508-1516.
Out of 160 OT‐VA cases (51±15‐year‐old, 62 males), 31 underwent HNS irrigation after a failed standard NS‐irrigated ablation

## Slide 6
CASE
RNH #1989619
30-year-old female, syncope with palpitation
4 times of RFCA for OT VT/PVC (RVOT & LVOT) at other hospital
No SHD, LVEF=55%

## Slide 7
CASE
RNH #1989619
Serial ECG changes
I
II
III
aVR
aVL
aVF
V1
V2
V3
V4
V5
V6

## Slide 8
CASE
RNH #1989619
Ablation at RCC, EA 21ms
EA 21ms
ABLd
ABLp

## Slide 9
CASE
RNH #1989619
Ablation at anteroseptum of RVOT
EA 26 ms
ABLd
ABLp
EA 26ms

## Slide 10
CASE
Bipolar ablation
RCC: Active ablation
RVOT: Return electrode
EA 29ms
ABL RCC d
ABL RCC p
ABL RVOT d
ABL RVOT p
LAO
RAO

## Slide 11
CASE
Bipolar ablation
RCC: Active ablation
RVOT: Return electrode
RF Generator
Patient Return Electrode
To Ablation Catheter
Indifferent Electrode EGM Recording

## Slide 12
CASE
During bipolar ablation
ABL RCC d
ABL RCC p
ABL RVOT d
ABL RVOT p
RNH #1989619

## Slide 13
CASE
After ablation
RNH #1989619

## Slide 14
Techniques for 2-site Ablation
Stevenson WG, et al. Can J Cardiol. 2022.
Simultaneous unipolar ablation
Bipolar ablation

## Slide 15
Bipolar Ablation between the Left Pulmonic Cusp (LPC) and LVOT for LV Summit VAs
Futyma P, et al. Heart Rhythm. 2020 Sep;17(9):1519-1527.
Seven patients (age 59±12 years; 3 women) underwent Bi-RF from the LPC to the LVOT for LVS-VAs after ≥1 failed conventional RFCA

## Slide 16
Needle RF Ablation: A First-in-Man Trial
Packer DL, et al. Circ Arrhythm Electrophysiol. 2022.
Intramural needle ablation using in-catheter, heated saline-enhanced radio frequency (SERF) energy
Thirty-two subjects from 6 centers (91% male, 66±10 years, EF 35±11%; 56% ischemic, and 44% nonischemic)
SERF needle electrode and ablation generator system

## Slide 17
Needle RF Ablation: A First-in-Man Trial
Packer DL, et al. Circ Arrhythm Electrophysiol. 2022.
Lesion creation with standard RF and SERF ablations

## Slide 18
Needle RF Ablation: A First-in-Man Trial
Packer DL, et al. Circ Arrhythm Electrophysiol. 2022.
Pre- and postprocedure VT occurrences and ICD therapies

## Slide 19
Needle RF Ablation: A First-in-Man Trial
Packer DL, et al. Circ Arrhythm Electrophysiol. 2022.
Adverse Events With Needle Electrode Ablation

## Slide 20
Intramural Venous Ethanol Infusion
Tavares L, et al. JACC Clin Electrophysiol. 2020.
Outcomes of a multicenter experience, n=63 (age 63±14 years; 60% men) with VAs (76% LVS origin)
Overall success in 55 of 56 (98%), 77% were free of recurrence at 1 year

## Slide 21
Intramural Venous Ethanol Infusion
Tavares L, et al. JACC Clin Electrophysiol. 2020.
LVS Ethanol Injection in Proximal LVS Veins

## Slide 22
Ultra-low-temperature Cryoablation (ULTC)
Sanchez-Somonte P, et al. HeartRhythm Case Rep. 2022 May 18;8(8):549-553.
Near-critical nitrogen has a much more favorable cryogenic properties and is able to generate temperatures as low as -196°C
Adagio Medical ULTC system
79-year-old man with ischemic VT

## Slide 23
Laser Energy Ablation Catheter
Krist D, et al. Front Med Technol. 2022.
Laser ablation catheter
The experimental 20mm linear laser catheter witha bidirectional steerable 8.2F shaft and saline irrigated tip
An in vivo proof-of-concept study in 6 swines
Epicardial ablation of the RV and LV

## Slide 24
Shock-Wave Catheter Ablation System
Morosawa S, et al. J Am Heart Assoc. 2019.
Characteristics of the SWCA system
Shock waves is an acoustic pressure wave consisting of a compressive phase (overpressure) followed by a tensile phase (negative pressure).
Shock waves can be applied to deep lesions without heat.
Validation Study in Pigs In Vivo

## Slide 25
Image-Based Simulations for VT Ablation
Trayanova NA, et al. Circ Arrhythm Electrophysiol. 2017.
Construction for heart model
VT ablation workflows
MRI–based simulation approach for VT ablation

## Slide 26
Future of VT Ablation
VG LIM. BCS Editorial 2020.